## Slide 1: Smart-Home Project
Presented by:
Eng. Shady Aly Soltan
Eng. Mohamed Bakr

## Slide 2: Table of Content
Introduction
Project Components
Communication Protocols
System Explanation
Flow Chart

## Slide 3: Introduction

## Slide 4: Introduction
What is a Smart Home?
Why Smart Home?
Is it Safe?
Objectives of Smart Home.

## Slide 5: Project Components

## Slide 6: Project Components
Two ATMEGA 32 Microcontrollers.
16 Bit LCD.
Keypad.
7 Led.
Bluetooth Module HC-05.
Servo Motor.
DC Motor.
24AA16 EEPROM.
Dimming Circuit.
LM25 Temperature Sensor.
Buzzer.

## Slide 7: Communication Protocols

## Slide 8: Communication Protocols
Single Master & Single Slave.
Asynchronous.
Admin Mode.
  Connect between MC and Mobile Phone by Bluetooth.
TX pin: Used to transmit data from MC to Mobile Phone
RX pin: Used to receive data from Mobile Phone to MC.
UART

## Slide 9: Communication Protocols
Single Master & Multi Slave.
Synchronous.
User Mode.
  Connect between Master MC and Slave MC.
MOSI: Used to transmit data from Master to Slave
MISO: Used to receive data from Slave to Master.
SS: Slave select pin, connect slaves to it.
SCLK: Clock Pin.
SPI

## Slide 10: Communication Protocols
Multi Master & Multi Slave.
Synchronous.
User & Admin Modes.
  Connect between MC and EEPROM.
  Save User Password.
  Save Door & Alarm last status.
SDA: Used to transmit & Receive data (Serial Data Line)
SCL: Clock Pin.
I2C

## Slide 11: System Explanation

## Slide 12: System Explanation
Admin Mode
Alarm
Check
  Check alarm status by location in EEPROM.
Door
Check
  Check Door status by location in EEPROM.
Admin
Menu
  Transmit admin menu to mobile phone using UART.
  Receive admin choice in Master Microcontroller.
Action
  Transmit action from master to slave MC using SPI.
  Transmit Alert MSG from master to mobile phone.
  Switch to User Mode if desired.
= 0xFF
!= 0xFF
= 0xFF
!= 0xFF
UART
Master
SPI
Slave
Door Action
I2C

## Slide 13: System Explanation
User Mode
Registration Menu
  Check password existence location in EEPROM.
Alarm
Check
  Check alarm status by location in EEPROM.
= 0xFF
!= 0xFF
Door
Check
  Check door status by location in EEPROM.
= 0xFF
!= 0xFF
= 0xFF
!= 0xFF
Login Menu
  Check entered password by user using keypad.
< 3Trials
> 3Trials

## Slide 14: System Explanation
User Mode
Action
  Print current status for LEDS & AC as a reminder.
  Print toggle option or return to Room menu.
  IF Toggle, Transmit action from master to slave MC using SPI & alert MSG to admin using UART.
  Return to room menu.
Main Menu
  Print on LCD (Room1 - Room2 - Admin - Lock).
    Room1: 2LEDS and Air Conditioner.
    Room2: 3LED one with Diming Circuit.
    Admin: Switch to Admin Mode.
    Lock: Ask for password before any action.
DIO
Master
Slave
Alert
SPI
UART

## Slide 15: Flow Chart

## Slide 16: Flow Chart

## Slide 17: Thank You
Presented by:
Eng. Shady Aly Soltan
Eng. Mohamed Bakr